## Slide 1
mPower Advisor
An agentic assistant for mPower users — from “the run finished” to “I know what to do next”
Automated triage of mpower.error.log, missing inputs, true warning roll-up counts and stage timing.
YOU RUN IT
Point it at a run
mpower-advisor <run_dir>
Reads logs_<timestamp>/ in place — any finished or historical run, no tool rebuild.
IT COLLECTS
Run Manifest
mpower.log · mpower.error.log · mpower.warning.log · mpower.lib.log · mpower.cmd · run.tcl · *.rpt
IT ANALYZES
Findings
Rules emit severity · code · count · evidence. The model correlates and ranks — never computes.
YOU GET
Run report
mpower_result_summary
.html dashboard, or .md to paste into a ticket.
OUTCOME A ranked “Recommended Next Actions” list — every number cited back to a file and line.
Draft for review · July 2026 · Siemens EDA — mPower

## Slide 2
What It Does
Four capabilities in the first release — each shown with real output from the BRCM rts_top reference run
1
Run digest / dashboard
“Did my run do what I asked, and can I trust the result?”
Run outcome Completed · final.db saved
Wall / peak mem 11h 18m · 98.7 GB
Worst dynamic IR 14.7% = 111.6 mV of 0.76 V
EM violations 0 Hard errors 4
2
Input & setup validation
“What did mPower silently work around?”
PWR-327 523,976 of 4,045,248 nets: no arrival time
PWR-297 Timescale is not defined in the TWF
warning No instances found in twf
→ 4,888 nets fell back to toggle_rate 0.07
3
Error triage
“It failed or looks wrong — why, and what do I change?”
Error: Clock ...u_rts_clk_rst_ctrl/dnt_ckbuf_rts_clk/o
already exist, command ignored × 4
→ mPower kept the first definition — on the same
block that has the worst dynamic IR (14.7%).
4
Performance advisor
“It took 11 hours. Where did the time go?”
Dynamic IR 50 ns @ 5 ps 7h 45m 69%
SPEF + TWF + Power 2h 08m 19%
→ 6.3h CPU vs 7.8h wall: not parallelizing well
→ distributed power off · 16 of 128 slots used
COMING NEXT
Phases 4–5
EM / IR-drop debug
“This instance violates — what causes it and what’s the fix?”
Needs hotspot ↔ power-density ↔ grid-R ↔ via-density correlation.
Setup assistant
“How do I set this flow up correctly in the first place?”
Needs a canonical flow model mined from the 826 regression runScripts.
Delivered as mpower_result_summary.html (dashboard) and .md (paste into a ticket).

## Slide 3
Architecture
Five layers — each independently useful and independently testable
INPUT
Run directory
mpower.log · mpower.error.log · mpower.warning.log · mpower.lib.log · mpower.cmd · run.tcl · *.rpt
L1
Collectors — discovery & normalization
Emits the Run Manifest: one versioned JSON that everything downstream consumes
L2
Knowledge base
1,767 .mhelp codes · 390 ghelp/*.help commands · 826 regression runScripts · playbooks
L3
Analyzers — deterministic rules → Findings
completeness · error triage · warning roll-up · performance · margin · config sanity
L4
Reasoning — LLM correlation & narrative
Cross-domain correlation, impact ranking, prose · + agentic tool-use (Phase 3+)
L5
Presentation
mpower_result_summary.html · mpower_result_summary.md · interactive chat
DESIGN PRINCIPLES
Deterministic first, LLM second
Every number comes from a parser. The model explains and ranks — never computes.
Cite everything
Every finding links to source file and line — auditable in one click.
Degrade gracefully
Crashed runs, partial runs, and runs with no report_time calls still report.
Offline-capable
Usable with no external network — and with no LLM at all.
Key decision: the Run Manifest decouples parsing from analysis — the whole system is testable without a single LLM call.

## Slide 4
Roadmap
What the user gets, in the order it ships
0
Groundwork Phase 0
Labeled corpus of 20–30 historical runs, the Run Manifest schema, a normalized .mhelp <type> field, and the eval harness.
2 EW
1
A run report you can trust Phase 1
Deterministic digest — KPIs, stage timing, max-of-roll-up warning counts, missing inputs. No LLM. Shippable to AEs on its own.
2–3 EW
2
It explains itself Phase 2
Cross-domain correlation, severity ranking and a prioritized next-actions list — strictly grounded, every claim cited.
2–3 EW
3
You can ask it questions Phase 3
Conversational follow-up (“show me the nets without_delay”), tool-use over the manifest, multi-run diff vs a prior run.
2–3 EW
4
It finds the root cause Phase 4
EM / IR-drop debug — hotspot clustering, blame attribution, decap adequacy, concrete mitigation proposals.
10–14 EW
5
It catches problems before you run Phase 5
Setup assistant — pre-flight flow validation, guided setup, an analyze_run Tcl command, GUI2 panel / CI gating.
6–10 EW
Runs alongside every phase — remediation knowledge (4–6 expert-weeks, not dev time): 976 of the 1,767 .mhelp codes carry <action> No_Information. Filling <action> for the top codes by frequency turns a finding into a fix.
First shippable value: ~4–5 EW (Phases 0+1) · Full vision: ~24–35 dev-EW ≈ 2 engineers × 3–4 months, plus 4–6 domain-expert weeks